## Commercial Air Source Heat Pump

Air Source Heat Pump   Commercial Air Source Heat Pump

Features of the Commercial Air Source Heat Pump
1. The heating capacity of commercial air source heat pump ranges from 11.2~87.4 kW. 
2. The air source heat pump is available with R407C/R410A or R22 refrigerants both environment friendly to offer high COP, up to 4.5.
3. This product uses Copeland scroll compressors and American tube and shell with high efficiency for heat exchanger. 
4. Our commercial air source heat pump applies Emerson Pump ALCO expansion valve, with accurate and stable throttling function. 
5. It presents high efficiency coaxial coil tube and shell heat exchanger with low fouling, and low maintenance cost.
6. The heat pump has durable coating, with fashionable design that adopts bolts and nuts, with no damage to the coating thus, avoiding rust 
7. The accurate casing for the fan shroud, with strictly equal distance between the fan blades and the fan shroud edge, largely reduce the vibration and noise.
8. The highest water outlet temperature of the commercial air source heat pump is 60℃.
9. This product has special modular system design with big units separated in 2 systems with separate compressors. Each system stays as a module and can start and work separately. 10. Our commercial air source heat pump saves running cost as high as 60%~80% compared to oil boiler, gas boiler, boiler, electric water heater and so on.
11. The whole units of this product are warranted for one year.
12. Powder coated cabinet is utilized for attractive appearance and economical purpose.
13. This product is able to connect with existing water system.
14. Our commercial air source heat pump is very easy to install with water pipes and can be connected with power socket simply 
15. The inlet water temp is of 15℃ and outlet water temp is 55℃, only on one time cycle.

Technical parameters of Commercial Air Source Heat Pump

| Model |  | KFRS-10I | KFRS-20II | KFRS-35II | KFRS-45II | KFRS-55II | KFRS-70II | KFRS-90II |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Power | HP | 3 | 5 | 10 | 12 | 16 | 20 | 25 |
| Heating capacity | kW | 11.20 | 18.00 | 36.30 | 43.70 | 54.40 | 69.80 | 87.40 |
|  | BTU/h | 38214 | 61416 | 123856 | 149104 | 185613 | 238158 | 298209 |
| COP |  | 4.67 | 4.62 | 4.65 | 4.62 | 4.69 | 4.58 | 4.64 |
| Rated heated water output | L/h | 241 | 387 | 780 | 939 | 1169 | 1500 | 1879 |
| Rated outlet water temp. | ℃ | 55 |
| Max outlet water temp | ℃ | 60 |
| Rated power input | kW | 2.40 | 3.90 | 7.80 | 9.45 | 11.60 | 15.23 | 18.85 |
| Rated current | A | 10.9 | 7.41 | 14.81 | 17.94 | 22.03 | 28.92 | 32.1 |
| Power supply | V/PH/Hz | 220V1N~/50Hz | 380V/3N~/50Hz |
| Compressor | Type | Scroll |
|  | Number | 1 | 1 | 2 | 2 | 2 | 2 | 2 |
| Heat exchanger type |  | High efficiency tube in shell heat exchanger |
| Throttling device |  | Emerson thermal expansion valve |
| Fan | Type | Low noise high efficiency axial type |
|  | Discharging | Vertical |
|  | Quantity | 1 | 1 | 2 | 2 | 2 | 2 | 2 |
|  | Power input/W | 70 | 250 | 250 | 250 | 550 | 750 | 750 |
|  | Speed/RPM | 850 | 880 | 880 | 880 | 910 | 940 | 940 |
| Ambient temperature | ℃ | (-10℃~43℃) |
| Refrigerant |  | R22/R407C |
| Noise in 1 meter distance | dB | 59 | 62 | 63 | 63 | 66 | 68 | 68 |
| Water pipe size | Inch | R1 | R1 | R1-1/2 | R1-1/2 | Rc2 | Rc2-1/2 | Rc2-1/2 |
| Cabinet |  | Stainless Steel/Steel with powder coated | Steel with powder coated |
| Low pressure protection system |  | Yes |
| High pressure protection system |  | Yes |
| Water flow switch |  | No |
| Automatically defrost system |  | Yes |
| Dimension | mm | 710/710 /795 | 810/810 /995 | 1450/705 /1375 | 1450/705 /1375 | 1445/850 /1850 | 1990/980 /2045 | 1990/980 /2045 |
| Package dimension | mm | 810/810 /980 | 920/920 /1080 | 1580/840 /1450 | 1580/840 /1450 | 1580/860 /2000 | 2090/1190 /2145 | 2090/1190 /2145 |
| Net weight | kg | 99 | 137 | 276 | 305 | 380 | 552 | 586 |
| Gross weight | kg | 115 | 160 | 316 | 345 | 440 | 622 | 656 |
| Testing condition: Ambient temp. (DB/WB) = 20℃/ 15 ℃, Inlet/outlet water temp. = 15℃/55℃ |

Heat pump supply Commercial air source heat pump is designed for offering hot water for commercial use, such as office, workshop, supermarket, school, and more. In order to achieve the required water temperature, large heat pump units that apply Unique "V" style evaporator design is a big strongpoint for this unit. It increases the evaporator space in air flow direction, which results in bigger effective air volume. It had been proved to be better efficiency by our testing. This design is also easier for the defrosting water to drain out. Scroll compressor with R410a/R22/R407c refrigerant is standard for this commercial air source heat pump. It is helpful to get better performance in low temperature.

Heat pump supply is a professional commercial air source heat pump manufacturer in China. Our company also provides household heat pump water heater, solar water heater, solar collector, split air source heat pump, and much more.

http://www.heatpumpsupply.com