## Swimming Pool Air Source Heat Pump

Air Source Heat Pump » Swimming Pool Air Source Heat Pump

General features 
1. Swimming pool air source heat pump has automatic operation mode
2. It features auto-restart and auto defrosting.
3. The heat pump has friendly and intelligent LCD Control panel interface.
4. Both cooling & heating mode are optional for this heat pump.
5. The product presents wide working ambient temperature, ranging from 10 ºC to 43ºC.
6. It adopts world famous Copeland compressor.
7. Finally it includes Green refrigerant R410a/R407c for environment safety etc.

Advantages of Swimming pool air source heat pump
1. The heating capacity ranges from 7kW, 220V/1ph/50Hz to 230kW, 380V/3ph/50Hz
2. The swimming pool air source heat pump has long operating life by using the advanced stainless steel/titanium heat exchanger, which resists the erosion from chlorine in the water and creates a longer life span. 
3. It is designed for comprehensive anti-corrosion feature, in which the special case design adopts stainless steel bolts and nuts. The holes for bolts are designed to avoid the damage of the coating. Durable coating in white or stainless steel is available 
4. Special design for the fan shroud, with accurate and equal distance between the fan blades and fan shroud, offers low vibration, and low noise when running.
5. The heat pump features intelligent defrosting with revert circuit.
6. This product has cover on remote wire control panel and is waterproof
7. The refrigerant available for our swimming pool air source heat pump is R22/ R407C/ R410A.
8. Our heat pump is remarkably compact with flow switch built inside.
9. Our swimming pool air source heat pump offers safety for both water and electricity by separating insulated part without electric shock.
10. The whole units of the product are warranted for one year period.

Technical Specification of Swimming Pool Heat and Chill Pumps - Vertical style

| Model | Units | HLRD 9-YC | HLRD 15-YC | HLRD 24-YC | HLRD 30-YC | HLRD 36-YC | HLRD 45-YC | HLRD 60-YC | HLRD 75-YC | HLRD 95-YC | HLRD 125-YC | HLRD 150-YC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Heating Capacity | kW | 13.5 | 21.3 | 35.5 | 45.5 | 52.8 | 66 | 87.4 | 110 | 140 | 191 | 230 |
|  | BTU/h | 46000 | 73000 | 121000 | 155000 | 180000 | 225000 | 300000 | 376000 | 480000 | 650000 | 785000 |
| COP | ---- | 4.33 | 4.96 | 4.87 | 4.84 | 4.74 | 4.46 | 4.65 | 4.73 | 4.87 | 5.08 | 4.94 |
| Cooling Capacity | kW | 8.8 | 14.7 | 25.5 | 30.5 | 35.8 | 44.9 | 59.5 | 75 | 95.2 | 126.9 | 150 |
|  | BTU/h | 30000 | 50000 | 87000 | 104000 | 122000 | 153000 | 203000 | 256000 | 325000 | 430000 | 512000 |
| EER | ---- | 2.67 | 2.68 | 3.00 | 2.78 | 3.12 | 2.78 | 2.71 | 2.80 | 3.20 | 2.89 | 2.79 |
| Max Water Outlet Temperature | ℃ | 45 |
| Power Supply | V/PH/HZ | 220-240V/1N~/50Hz | 380V-400V/3N~ /50Hz |
| Rated Input Power (Heating/Cooling) | kW | 3.12/ 3.30 | 4.3/ 5.50 | 7.30/ 8.50 | 9.4/ 11.00 | 11.15/ 11.50 | 14.80/ 16.20 | 18.80/ 22.00 | 23.30/ 26.80 | 28.80/ 29.80 | 37.60/ 44.00 | 46.60/ 53.80 |
| Rated Input Current (Heating/ Cooling) | A | 14.5/ 15.3 | 6.5/ 9.9 | 11/ 13.4 | 14.2/ 19.8 | 20.1/ 19.24 | 28.2/ 30.1 | 33.9/ 39.7 | 42.0/ 48.3 | 51.92/ 53.7 | 67.8/ 79.4 | 84.00/ 96.6 |
| Max Input Power | kW | 3.4 | 6.1 | 10 | 13.5 | 15.1 | 18.9 | 25.4 | 31.5 | 38.75 | 50.8 | 63 |
| Max Input Current | A | 15.5 | 9.2 | 15.2 | 20.6 | 27.2 | 34.1 | 45.8 | 56.8 | 69.86 | 91.6 | 113.6 |
| Ambient Temperature | ℃ | -10℃~43℃ |
| Heat Exchanger |  | Titanium in seamless stainless steel |
| Refrigerant/Chare Qty | kg | R407C /1.5 | R407C /1.9 | R407C /1.7*2 | R407C /3.8 | R407C /2.2*2 | R407C /3.5*2 | R407C /4.5*2 | R407C /5.5*2 | R407C /6.5*2 |  |  |
| Compressor Type |  | Scroll |
| Number of Compressors |  | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 4 | 4 |
| Number of Fans |  | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 4 | 4 |
| Fan Air Flow Volume | m3/h | 3900 | 6500 | 13000 | 13000 | 15600 | 19500 | 26000 | 32500 | 39000 | 65600 | 78000 |
| Fan Direction |  | Vertical |
| Fan Power Input | W | 180 | 260 | 320×2 | 320×2 | 550×2 | 550×2 | 640x2 | 1100x2 | 1100x2 | 640x4 | 1100x4 |
| Fan Rotation Speed | RPM | 850 | 850 | 790 | 790 | 820 | 820 | 790 | 820 | 820 | 790 | 820 |
| Noise | dB (A) | ≤54 | ≤56 | ≤61 | ≤61 | ≤66 | ≤66 | ≤66 | ≤68 | 68 | 71 | 72 |
| Piping Diameter | mm | DN40 | DN40 | DN50 | DN50 | DN50 | DN65 | DN65 | DN80 | DN80 | DN80 | DN100 |
| Discharge Pressure | Mpa | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 | 2.5 |  |  |
| Suction Pressure | Mpa | 0.3-0.8 | 0.3-0.8 | 0.3-0.8 | 0.3-0.8 | 0.3-0.8 | 0.3-0.8 | 0.3-0.8 | 0.3-0.8 | 0.3-0.8 |  |  |
| Rated Water Pressure | Mpa | 0.2~0.6 |
| Max Water-in Pressure | Mpa | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |  |
| Min Water-in Pressure | Mpa | / | / | / | / | / | / | / | / | / |  |  |
| Water Flow Volume | m3/h | 2.52 | 3.77 | 6.00 | 7.54 | 9.05 | 11.31 | 14.98 | 18.86 | 24.00 | 32.74 | 39.43 |
| Net Weight | kg | 90 | 114 | 214 | 244 | 276 | 450 | 472 | 680 | 720 | 944 | 1360 |
| Shipping Weight | kg | 102 | 128 | 238 | 268 | 316 | 487 | 526 | 734 | 785 | 1052 | 1468 |
| Product Dimension | mm | 695 /655 /740 | 703 /687 /930 | 1450 /705 /965 | 1450 /705 /1065 | 1450 /710 /1255 | 1580 /850 /1570 | 1990 /980 /2050 | 1990 /980 /2050 | 1900 /1020 /2050 | 2015 /2200 /2025 | 2015 /2200 /2025 |
| Shipping Size | mm | 787 /775 /842 | 816 /797 /1045 | 1535 /835 /1083 | 1535 /835 /1184 | 1560 /830 /1355 | 1700 /970 /1670 | 2110 /1100 /2150 | 2110 /1100 /2150 | 2120 /1140 /2150 | 2115 /2300 /2075 | 2115 /2300 /2075 |
| Certificates |  | CE/CB/C-TICK/SAA | CE |  |  |
| Notes: |  |  |  |  |  |  |  |  |  |  |  |  |
| 1. Heating working condition: Outdoor DB/WB temp: 24℃/19℃,62.5%RH, inlet/outlet water temp:27℃/32℃. |
| 2. Cooling working condition: Outdoor DB/WB temp: 43℃/37℃,68%RH, inlet/outlet water temp:32℃/27℃. |
| 3. Other sizes are available. 4. COP = heating capacity / heating power input (for heating). |  |  |  |  |  |
| 5. EER = cooling capacity / cooling power input (for cooling). |  |  |  |  |  |
| 6. Sizing: P= (CV (T2-T1)/t)*1.20 where P=Capacity required (kW), C=Coefficient (1.163), V=Water volume (m³), T2=Target water temp (°C), T1=Water temp before heating (°C), t=time to heat, plus add 20%. |

Technical specification of Swimming Pool Heat and Chill Pumps- Horizontal style

| Model | Units | HLRC5-YC | HLRC8-YC | HLRC9-YC | HLRC15-YC |
| --- | --- | --- | --- | --- | --- |
| Heating Capacity | kW | 7 | 9.8 | 13.5 | 21.3 |
|  | BTU/h | 24000 | 33400 | 46000 | 73000 |
| COP | ---- | 4.83 | 4.76 | 4.33 | 4.96 |
| Cooling Capacity | kW | 4.5 | 6.2 | 8.8 | 14.7 |
|  | BTU/h | 15000 | 21000 | 30000 | 50000 |
| EER | ---- | 2.73 | 2.82 | 2.67 | 2.68 |
| Max Water Outlet Temperature | ℃ | 45 |
| Power Supply | V/ph/Hz | 220-240V/1N~/50Hz | 380V-400V/3N~/50Hz |
| Rated Input Power (Heating/Cooling) | kW | 1.45/1.65 | 2.06/2.20 | 3.12/3.30 | 4.3/5.50 |
| Rated Input Current (Heating/ Cooling) | A | 6.6/7.5 | 9.6/10.2 | 14.5/15.3 | 6.5/9.9 |
| Max Input Power | kW | 1.9 | 2.5 | 3.4 | 6.1 |
| Max Input Current | A | 9.1 | 11.5 | 15.5 | 9.2 |
| Ambient Temperature | ℃ | -10℃~43℃ |
| Heat Exchanger |  | Titanium in seamless stainless steel |
| Refrigerant/Charge Qty | kg | R407C/1.1 | R407C/1.1 | R407C/1.5 | R407C/1.9 |
| Compressor Type |  | Rotary | Scroll |
| Number of Compressors |  | 1 | 1 | 1 | 1 |
| Number of Fans |  | 1 | 1 | 1 | 2 |
| Fan Air Flow Volume | m3/h | 2000 | 2600 | 3900 | 6500 |
| Fan Direction |  | Horizontal |
| Fan Power Input | W | 90 | 120 | 180 | 130x2 |
| Fan Rotation Speed | RPM | 850 | 850 | 850 | 850 |
| Noise | dB (A) | ≤48 | ≤50 | ≤54 | ≤56 |
| Piping Diameter | mm | DN25 | DN25 | DN40 | DN40 |
| Discharge Pressure | Mpa | 2.5 | 2.5 | 2.5 | 2.5 |
| Suction Pressure | Mpa | 0.3-0.8 | 0.3-0.8 | 0.3-0.8 | 0.3-0.8 |
| Rated Water Pressure | MPa | 0.2~0.6 |
| Max Water-in Pressure | Mpa | 1 | 1 | 1 | 1 |
| Min Water-in Pressure | Mpa | / | / | / | / |
| Water Flow Volume | m3/h | 1.20 | 1.68 | 2.31 | 3.65 |
| Net Weight | Kg | 38 | 67 | 97.5 | 114 |
| Shipping Weight | Kg | 51 | 85 | 113.5 | 128 |
| Product Dimension | mm | 1150/350/620 | 1150/350/620 | 1115/425/710 | 1110/420/1222 |
| Shipping Dimension | mm | 1200/400/670 | 1200/400/670 | 1242/540/782 | 1220/530/1337 |
| Certificates |  | CE | CE/CB/C-TICK/SAA |
| Notes: |  |  |  |  |  |
| 1. Heating working condition: Outdoor DB/WB temp: 24℃/19℃, 62.5%RH, inlet/outlet water temp:27℃/32℃. |
| 2. Cooling working condition: Outdoor DB/WB temp: 43℃/37℃, 68%RH, inlet/outlet water temp: 32℃/27℃. |
| 3. Other sizes are available. |  |  |  |  |  |
| 4. COP = heating capacity / heating power input (for heating). |  |  |  |
| 5. EER = cooling capacity / cooling power input (for cooling). |  |  |  |
| 6. Sizing: P= (CV (T2-T1)/t)*1.20 where P=Capacity required (kW), C=Coefficient (1.163), V=Water volume (m³), T2=Target water temp (°C), T1=Water temp before heating (°C), t=time to heat, plus add 20%. |

The swimming pool air source heat pump can be installed in many environments, including a constant temperature swimming pool, sauna constant hot water system, or for application of supplying hot water at home.

Heat pump supply is a swimming pool air source heat pump manufacturer in China. Our company provides a wide range of products including DC inverter air source heat pump, household heat pump water heater, and tube solar water heater, among others.

http://www.heatpumpsupply.com