Heat Pump Dryer

Heat Pump Dryer for Industrial Use

Model Number: DE-46W/K

MOQ: 1 Set

Key Specifications/Special Features:

- Parameters:

  - Outdoor unit:

    - Power supply: 380V/3ph/50Hz

    - Heating capacity: 18.5kW

    - Rated power input: 5.8kW

    - Ambient air volume: 5,500m³/hour

    - Refrigerant type: R417A

    - Refrigerant weight: 4,700g

    - Maximum input power: 10.5kW

    - Maximum current: 18.5A

    - Level against electric: shock I

    - Waterproof grade: IPX4

    - Net weight: 155kg

    - Net size: 800 x 800 x 1,000mm

    - Connection (φ): 12.7/19.05

    - Operating temperature range: -10 to 45°C

    - Noise: ≤62dBa

    - Test condition ambient temperature (dry/wet ball): 20/15°C

    - Outlet temperature: 45°C

  - Indoor unit:

    - Power supply: 380V/3ph/50Hz

    - Rated power input: 0.55kW

    - Maximum input power: 23.5kW

    - Level against electric: shock I

    - Waterproof grade: IPX4

    - Net weight: 100kg

    - Net size: 800 x 755 x 900mm

    - Operating temperature range: -10 to 45°C

    - Test condition ambient temperature (dry/wet ball): 20/15°C

    - Outlet temperature: 45°C

- Features:

  - Industrial use to bake, such as, tobacco, fruit, tea leaf, food, wood and more

  - An intelligent device comprises indoor and outdoor unit, integrating heating, cooling, moisture discharge and ventilation

  - Using the principle of heat pump for heat recovery from vapor condensation, no waste heat emission

  - Maximum outlet temperature is 45°C

- Composition:

  - Indoor unit includes Chinese famous brand FLH fan coil and fin type heat exchanger

  - Outdoor unit comprises Copeland compressor, Emerson ALCO expansion valve, anti-corrosion fin type evaporator

  - Refrigerant: R417a

Payment Details:

- Payment Terms:

  - Telegraphic Transfer (TT,T/T)

- Minimum Order:

  - 1 Set

Delivery Details:

- FOB Port:

  - Qingdao/Shanghai/Guangzhou

- Lead Time:

  - 20 - 25 days

Country of Origin:

- China (mainland)

Primary Competitive Advantages:

- Brand-name Parts

- Green Product

- Product Features

- Product Performance

- Quality Approvals

- Low-cost

- 18 Months Warranty

Main Export Markets:

- Eastern Europe

- Mid East/Africa

- Asia

- Western Europe

- Australasia

Http://www.heatpumpsupply.com/Heat-Pump-Dryer-for-Industrial-Use.htm

Contact us today.

www.heatpumpsupply.com