## Household Heat Pump Water Heater

Air Source Heat Pump » Household Heat Pump Water Heater

Features of Household Heat Pump Water Heater
1. The household heat pump water heater is designed with built-in highly efficient tube and shell heat exchanger and WILO water pump.
2. It features compact design, easier installation, and it takes up less space. 
3. All pipes have thermal insulation and low heat loss. 
4. Our household heat pump water heater has high efficiency reverse circuit design with auto defrosting function. 
5. The LCD wire controller is installed indoor to be convenient for users. 
6. This product adopts 304# Stainless steel cabinet, with anti corrosion and durable effect.

Application
Household heat pump water heater is suitable for family usage, application in villa, apartment, high-floor residence, restaurant, hotel and multi-floor living building for heating and sanitary hot water use.

Technical specification of Household Heat Pump Water Heater

| Model |  | KF80-B | KF120-B | KF240-B | KF400-B | KF480-B |
| --- | --- | --- | --- | --- | --- | --- |
| Power | HP | 1 | 1.5 | 3 | 5 | 6 |
| Heating capacity | kW | 3.71 | 5.58 | 11.6 | 19.1 | 18.1 |
|  | BTU/h | 12659 | 19039 | 39579 | 65169 | 61757 |
| COP |  | 4.12 | 4.46 | 4.64 | 4.24 | 4.11 |
| Rated heated water output | L/h | 80 | 120 | 240 | 400 | 480 |
| Rated outlet water temp. | ℃ | 55 |
| Max outlet water temp. | ℃ | 60 |
| Rated power input | kW | 0.9 | 1.25 | 2.5 | 4.5 | 4.4 |
| Rated current | A | 3.73 | 5.89 | 11.36 | 6.45 | 25.2 |
| Power supply | V/PH/Hz | 220V/1N~/50Hz | 380V/3N~/50Hz |  |
| Compressor | Type | Rotary | Scroll |
|  | Number | 1 | 1 | 1 | 1 | 2 |
| Heat exchanger type | Number | High efficiency tube in shell heat exchanger |
| Throttling device |  | Capillary | Emerson thermal expansion valve |
| Fan | Type | Low noise high efficiency axial type |
|  | Discharging | Horizontal | Horizontal/Vertical | Vertical |
|  | Quantity | 1 | 1 | 1 | 2 | 2 |
|  | Power input/W | 20 | 20 | 50 | 90 | 160 |
|  | Speed/RPM | 830 | 830 | 850 | 850 | 850 |
| Ambient temperature | ℃ | (-10℃~43℃) |
| Refrigerant |  | R22/R410A | R22/R407C |
| Noise in 1 meter distance | dB | ≤54dB(A) | ≤54dB(A) | ≤59dB(A) | ≤62dB(A) | ≤62dB(A) |
| Water pipe size | inch | Rc3/4 | Rc3/4 | R1 | R1 | R1-1/2 |
| Suggested water tank capacity | L | 100-150 | 200-300 | 300-500 | 500 | 500 |
| Cabinet |  | Stainless steel |
| Low pressure protection system |  | Yes |
| High pressure protection system |  | Yes |
| Water flow switch |  | No |
| Automatically defrost system |  | Yes |
| Product Dimension | mm | 710/310/940 | 710/310/940 | 800/400/1220 | 1110/530/1260 | 1430/700/860 |
|  | (left-right)mm | 930/360/560 | 930/360/560 | 760/700/860 |  |  |
| Package dimension | mm | 850/450/1020 | 850/450/1020 | 950/550/1400 | 1260/680/1430 | 1570/840/1050 |
|  | (left-right)mm | 1080/450/660 | 1080/450/660 | 900/830/1050 |  |  |
| Net weight | kg | 55 | 62 | 110 | 155 | 190 |
|  | (left-right)mm | 48 | 55 | 95 |  |  |
| Gross weight | kg | 67 | 74 | 134 | 178 | 249 |
|  | (left-right)mm | 58 | 65 | 139 |  |  |
| Testing condition: Ambient temp.(DB/WB) = 20℃/ 15 ℃, Inlet/outlet water temp. = 15℃/55℃ |

Our household heat pump water heater adopts high efficiency tube and shell heat exchanger and has built in water pump inside the heat pump unit. This ensures not only high efficiency performance of the system but also easy installation of work. This product is different from other ordinary domestic Split System which is simply installed to connect to the heat pump unit and then to the water tank through water piping. The refrigerant pipe connection work will not be necessary to heat the water. The water tank connection with this heat pump does not have copper coil heat exchanger inside, which saves the cost of water tank.

As a manufacturer and supplier specialized in household heat pump water heater in China, Heat pump Supply also provides commercial air source heat pump, split air source heat pump, solar water heater, among others.

http://www.heatpumpsupply.com