Air to Water Heat Pump

High-temperature Hot Water Series, Low-ambient Air to Water Heat Pump, Efficient in -25°C

Model Number: DE-46W/DGW

Key Specifications/Special Features:

- Power supply: 380ph/3V/50Hz

- Heating capacity: 14kW

- Rated power input: 4kW

- Water temperature:

  - Maximum water temperature: 75°C (default)

  - Adjustable range: 40 to 80°C (new)

- Refrigerant type: R134A (new)

- COP up to 4.0

- Compressor: copland ZW series EVI technology compressor

- Expansion valve: Emerson ALCO thermal expansion valve

- Heat exchanger: Tube in tube heat exchanger

- Case materials: coated steel/#304 stainless steel, avoiding rust effectively and durable

- It enable the heat pump to work well even when the ambient temperature is as low as -25°C

- OEM orders are welcome

Payment Details:

- Payment Terms:

  - Telegraphic Transfer in Advance (Advance TT, T/T)

Delivery Details:

- FOB Port:

  - Qingdao /Shanghai

- Lead Time:

  - 20 - 25 days

Country of Origin:

- China (mainland)

Primary Competitive Advantages:

- Brand-name Parts

- Country of Origin

- Distributorships Offered

- Green Product

- Guarantee/Warranty

- International Approvals

- Product Performance

- Quality Approvals

- Service

- 18-month Warranty

Main Export Markets:

- Eastern Europe

- Mid East/Africa

- Asia

- Western Europe

- Australasia

Contact us today.

www.heatpumpsupply.com

Other related products for air to water heat pump:

air to water heat pump

air to water heat pumps

air water heat pump

water to air heat pump

water heat pump

air water heat pumps

hot water heat pump

water to water heat pump

water heat pumps

air heat pump

air source heat pump

geothermal heat pumps

air source heat pumps

heat pump air to water

ground source heat pumps

air to water heating system

air to air heat pump

heat pump

air to air heat pumps

ground source heat pump

air to water heat pump prices

air to water heat pump manufacturers

air to water heat pump price

heat pump efficiency

heat pumps prices

air heat pumps

air to water heat pump cost

heat pump system

heat pump systems

heating pumps

what is a heat pump

heat pump installation

heat pump manufacturers

heat pump air water

heat pumps air

ground heat pumps

heat pumps cost

water source heat pump

heat pumps air to water

hot water heat pumps

air to water heat pump how it works

danfoss heat pumps

air to water heating

inverter heat pump

air to water heat pump system

air to water source heat pump

air to water heat exchanger

water source heat pumps

air to heat pumps

pool heat pump

air source heat pump water heater

geothermal heat pump

water heat pump system

pool heat pumps

heat pump air source

swimming pool heat pump

water heating

heat pumps

heat pump installation cost

ground to water heat pump

air to heat pump

air source heat pump problems

electric heat pump

gshp

geothermal heat pump cost

water to water heat pumps

solar water heating

air source heating

swimming pool heat pumps

air to water heating systems

water air heat pump

ground source heat pump cost

heat pump water heater

насосы для отопления

heat pump cost

heat pump prices

portable heat pump

heat pumps for pools

heatpump

water cooled heat pump system

solar heat pump

water furnace heat pumps

heat pumps air source

air heat pump prices

air source heat pump manufacturers

water heater heat pump

residential heat pumps

water heat

air water pumps

heat pumps for sale

bosch heat pumps

heat pump reviews

air to water pump

heatpumps

air source heat pump cost

water to water heat pump water heater

heat pump for water heating

home heat pumps

hot water heat

heat pump hot water

ductless heat pump

from

www.heatpumpsupply.com

By Heat Pump Supply on May 21, 2013

Contact us today: info@savegreeninc.com

We supply air to water heat pumps, please check our website for more information:

www.savegreeninc.com