## Split Air Source Heat Pump

Home » Products » Air Source Heat Pump » Split Air Source Heat Pump

Heat pump supply Luxury split air source heat pump provides energy-efficient space heating, cooling and domestic hot water for residential and small commercial application. Adopting the Green refrigerant R410a for highly efficient with low running costs, low carbon emission hence enabling it to be integrated with energy systems such as solar heater and boiler. The split design has no water system outside, any freezing or damage to water system. All hydraulic parts are located within the indoor unit. Parts such as water pump, expansion vessel, buffer tank and safety equipment have already been fitted inside the indoor unit. Optional refrigerant pipe quick connection is available to reduce installation cost.

Application of Split Air Source Heat Pump
Heat pump supply split system heat pump also can be installed in both new and renewal applications. If you already have the heating system there is no need to change it. The split system of heat pump can be compatible with.
a. Floor heating and cooling.
b. Fan-coils.
c. Mixed installation for floor heating and fan-coils.
d. Standard low temperature radiators.
e. Thermal solar energy among others.

Technical Specification of Split Air Source Heat Pump

| TECHNICAL DATA | NT-11HAS | NT-14HAS | NT-16HAS/3 |
| --- | --- | --- | --- |
| Heating | Nominal capacity | kW | 11.52 | 13.73 | 16.02 |
|  | Power input | kW | 3.25 | 3.38 | 4.01 |
|  | COP | W/W | 3.55 | 4.06 | 4.00 |
| Cooling | Nominal capacity | kW | 10.29 | 13.01 | 14.74 |
|  | Power input | kW | 3.85 | 4.16 | 4.98 |
|  | EER | W/W | 2.67 | 3.13 | 2.96 |
| DHW | Nominal capacity | kW | 10.06 | 12.58 | 15.21 |
|  | Power input | kW | 3.95 | 4.05 | 4.88 |
|  | COP | W/W | 2.55 | 3.11 | 3.12 |
| Power supply | V/Ph/Hz | 220-240/1/50 | 380-415/3/50 |
| Max. leaving water temperature (without using backup heater) | ℃ | 58 |
| Refrigerant | R410A |
| Compressor | Type |  | Scroll |
|  | Brand |  | SANYO | DAIKIN | DAIKIN |
| Dimensions (Net) | Indoor unit mm | mm | 1047x508x406 |
|  | (HeightxWidthxDepth ) |  |  |
|  | Outdoor unit mm | mm | 960x990x360 | 960x990x360 | 1225x950x360 |
|  | (HeightxWidthxDepth ) |  |  |  |  |
| Dimensions (Packing) | Indoor unit mm | mm | 1120x585x470 |
|  | (HeightxWidthxDepth ) |  |  |
|  | Outdoor unit mm | mm | 1100x1105x420 | 1100x1105x420 | 1380x1045x455 |
|  | (HeightxWidthxDepth ) |  |  |  |  |
| Net weight | Indoor unit | kg | 67 | 68 | 69 |
|  | Outdoor unit | kg | 95 | 98 | 113 |
| Gross weight | Indoor unit | kg | 71 | 72 | 73 |
|  | Outdoor unit | kg | 103 | 106 | 122 |
| Noise level | Indoor unit | dB(A) | 31 |
|  | Outdoor unit | dB(A) | 51 | 54 | 55 |
| Container loading | 20' GP | 34 (units) | 34 (units) | 27 (units) |
|  | 40' GP | 72 (units) | 72 (units) | 57 (units) |
|  | 40' HQ | 72 (units) | 72 (units) | 57 (units) |
| Features included |  |
| ON/OFF or Inverter type | On/off unit |
| Plate heat exchanger | Stainless steel heat exchanger |
| Water pump | Wilo brand 4.6 m3/hr |
| 3-way valve | Switch from space heating/cooling to domestic hot water |
| Manometer | Refrigerant/water pressure manometer |
| Stainless steel buffer tank | 20L |
| Expansion vessel | 10 L |
| Electric heater | 3*2kW |
| Castel safety valve | yes |
| Castel air purge valve | yes |
| Water flow switch | yes |
| Auto restart | yes |
| Notes: Capacities and power inputs based on the following conditions: - Heating: Water Inlet/Outlet in temperature of 30℃ /35℃ . Outdoor air dry bulb/wet bulb temperature ranges from 7℃ to 6℃ - Cooling: Water Inlet/Outlet in temperature of 23℃ /18℃ . Outdoor air dry bulb temperature is 35℃ - Domestic Hot Water: Water temperature in the tank is 40℃ . Outdoor air dry bulb/wet bulb temperature is 7℃ /6℃ - Data are based on approx 5 m length of well insulated refrigerant pipes. Refrigerant content is suitable for 10 meters long pipes. |

Heat pump supply is an experienced split air source heat pump manufacturer in China. Our company provides household heat pump water heater, solar water heater, tube solar water heater, solar collector, among others.

Http://www.heatpumpsupply.com

Contact us now for quotation and order today.