## Direct Heating Commercial Air Source Heat Pump

Air Source Heat Pump » Direct Heating Commercial Air Source Heat Pump

Main Features and Advantages of Direct Heating Commercial Air Source Heat Pump
1. The heating capacity of our direct heating commercial air source heat pump ranges from 11.2~87.4 kW.
2. The air source heat pump is available with R407C/R410A or R22 refrigerants both environment friendly to offer high COP, up to 4.5.
3. This product uses Copeland scroll compressors and American tube and shell heat exchanger which feature high efficiency. 
4. Our direct heating commercial air source heat pump applies Emerson Pump ALCO expansion valve, with accurate and stable throttling function.
5. It presents high efficiency coaxial coil tube and shell heat exchanger with low fouling, and low maintenance cost.
6. This product has durable coating, with fashionable design that adopts bolts and nuts, with no damage to the coating which helps avoiding rust. 
7. The accurate casing for the fan shroud, with strictly equal distance between the fan blades and the fan shroud edge, largely reduce the vibration and noise.
8. The highest water outlet temperature of the direct heating commercial air source heat pump is 60℃.
9. This product has special modular system design with big units separated in 2 systems with separate compressors. Each system stays as a module and it can start and work separately. 
10. Big units adopting Unique "V" style evaporator design is a big strongpoint for the unit. It increases the condenser space in air flow direction, which results in bigger effective air volume. It had been proved to be better efficiency by our testing. This design is also easier for the defrosting water to drain out. 
11. Our direct heating commercial air source heat pump saves running cost as high as 60%~80% compared to oil boiler, gas boiler, boiler, electric water heater etc.
12. The whole units of this product are warranted for one year.
13. Powder coated cabinet is utilized for attractive appearance and economical purpose.
14. This product is able to connect with existing water system.
15. The air source heat pump is very easy to install with water pipe and its power can be connected to the socket safely. 
16. The product uses built-in solenoid valve to prevent passive flowing at hot water side.
17. The inlet water temp is of 15℃ and outlet water temp is 55℃, only on one time cycle.

Application
Our direct heating commercial air source heat pump can provide heating and hot water for commercial places where need much hot water and heating function, such as hotel, factory, school, hospital, military, villa, village and more.

Technical Specification of Direct Heating Commercial Air Source Heat Pump

| Model |  | KFS10-N-JR | KFS20-N-JR | KFS35-N-JR | KFS45-N-JR | KFS55-N-JR | KFS70-N-JR | KFS90-N-JR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Power | HP | 3 | 5 | 10 | 12 | 16 | 20 | 25 |
| Heating capacity | kW | 11.20 | 18.00 | 36.30 | 43.70 | 54.40 | 69.80 | 87.40 |
|  | BTU/h | 38214 | 61416 | 123856 | 149104 | 185613 | 238158 | 298209 |
| COP |  | 4.67 | 4.62 | 4.65 | 4.62 | 4.69 | 4.58 | 4.64 |
| Rated Heated water output | L/h | 241 | 387 | 780 | 939 | 1169 | 1500 | 1879 |
| Rated outlet water temp. | ℃ | 55 |
| Max outlet water temp | ℃ | 60 |
| Rated power input | kW | 2.40 | 3.90 | 7.80 | 9.45 | 11.60 | 15.23 | 18.85 |
| Rated current | A | 10.9 | 7.41 | 14.81 | 17.94 | 22.03 | 28.92 | 32.1 |
| Power supply | V/PH/Hz | 220V~/50Hz | 380V/3N~/50Hz |
| Compressor | Type | Scroll |
|  | Number | 1 | 1 | 2 | 2 | 2 | 2 | 2 |
| Heat exchanger type |  | High efficiency tube in shell heat exchanger |
| Throttling device |  | Emerson thermal expansion valve |
| Fan | Type | Low noise high efficiency axial type |
|  | Discharging | Vertical |
|  | Quantity | 1 | 1 | 2 | 2 | 2 | 2 | 2 |
|  | Power input/W | 70 | 250 | 250 | 250 | 550 | 750 | 750 |
|  | Speed/RPM | 850 | 880 | 880 | 880 | 910 | 940 | 940 |
| Ambient temperature | ℃ | (-10℃~43℃) |
| Refrigerant |  | R22/R407C |
| Noise in 1 meter distance | dB | 59 | 62 | 63 | 63 | 66 | 68 | 68 |
| Water pipe size | Inch | R1 | R1 | R1-1/2 | R1-1/2 | Rc2 | Rc2-1/2 | Rc2-1/2 |
| Cabinet |  | Stainless Steel/Steel with powder coated | Steel with powder coated |
| Low pressure protection system |  | Yes |
| High pressure protection system |  | Yes |
| Water flow switch |  | No |
| Automatically defrost system |  | Yes |
| Dimension | mm | 710/710/795 | 810/810/995 | 1450/705/1375 | 1450/705/1375 | 1445/850/1850 | 1990/980/2045 | 1990/980/2045 |
| Package dimension | mm | 810/810/980 | 920/920/1080 | 1580/840/1450 | 1580/840/1450 | 1580/860/2000 | 2090/1190/2145 | 2090/1190/2145 |
| Net weight | kg | 99 | 137 | 276 | 305 | 380 | 552 | 586 |
| Gross weight | kg | 115 | 160 | 316 | 345 | 440 | 622 | 656 |
| Testing condition: Ambient temp.(DB/WB) = 20℃/ 15 ℃, Inlet/outlet water temp. = 15℃/55℃ |

Heat pump supply is a professional manufacturer of direct heating commercial air source heat pump based in China. Our products include household heat pump water heater, solar collector, solar water heater, and much more.