Heat Pump

New Design EVI Heat Pump, Fashionable, Efficient in -25°C, 11.6kW

Model Number: DE-27W/CW-EUO

MOQ: 1 Unit

Key Specifications/Special Features:

- Description:

  - Efficient in cold climate area, in low-ambient temperature: -25ºC

  - Adopted EVI technology: the latest innovation for heat pump products

- Components:

  - Compressor: Copeland ZW series new designed scroll compressor

  - Heat exchanger: coaxial coil heat exchanger

  - Expansion valves: Emerson

  - 4-way valve: Saginomiya

  - Two doors can be open from front/back side

  - Connections, name plate and brand logo is on the right side

  - Fan unit is on the front side, evaporator is only on the backside

  - No screw on the top of the heat pump

  - Lower noise

  - There is an anti-shock pad under the compressor and tables all over the bottom inside the case

- Parameters:

  - Refrigerant: R417A

  - Power supply: 220V/1ph/50Hz

  - Maximum water temperature: 60°C

  - Net size (L x W x H): 853 x 570 x 1,480mm

  - Colors: black, white and grey

  - Warranty: 18 months for the whole unit

Payment Details:

- Payment Terms:

  - Telegraphic Transfer in Advance (Advance TT, T/T)

- Minimum Order:

  - 1 Unit

Delivery Details:

- FOB Port:

Guangzhou/Shanghai/QingdaoCountry of Origin:

- China (mainland)

Primary Competitive Advantages:

- Brand-name Parts

- Distributorships Offered

- Experienced Staff

- Green Product

- Product Features

- Product Performance

- Service

Main Export Markets:

- Eastern Europe

- Mid East/Africa

- Asia

- Western Europe

- Lead Time:

  - 25 - 30 days

http://www.heatpumpsupply.com/New-Design-EVI-Heat-Pump-Fashionable-Efficient-in-minus-25-degree-centigrade-11-6kW.htm

Contact us today.

www.heatpumpsupply.com